Guidelines and Criteria for re-directing Network Integration Transmission Service (NITS)

In order to have the ability to re-direct NITS a customer must first have a reservation from a specific Designated Network Resource (DNR).

- The DNR must be for a resource that the customer has listed on their DNR list with their NITS agreement.

- SPP staff will create a reservation for the customer. (The source will not be a TSIN registered source and not available for tagging or on the OASIS pull down menu. The source will be the unit name with _DNR added to the end. For example: Tulsa2 becomes Tulsa2_DNR.) Note: The customer will not be able to submit the request due to Attachment P timing requirements if the start date of the NITS is in the past or if the start of the NITS is within 60 days of start.

- The start/stop dates will be concurrent with the NITS agreement dates.

- The mw value may not exceed the amount listed on the DNR list.

- SPP staff will create a sub-zone for the DNR. (Due to limitations in the EMS system this is limited to 20 sub-zones. A grouping of resources may be in the same sub-zone. For example Tulsa2_DNR, Tulsa3_DNR and Tulsa4_DNR may be in the same sub-zone)

- When a redirect is submitted for a DNR there must also be an outage or de-rate listed in OPS1 for that DNR that coincides with the time of the redirect. (The purpose of the redirect is to replace a DNR that is unavailable and to receive credit for the impact of that DNR to the system. If the DNR is redirected and still runs then the impacts on the system are doubled.)

Summary of steps for redirecting NITS

- NITS customer selects specific DNR they want to redirect.

- Customer provides the DNR and their suggested sub-zone groupings if there is more than one to SPP staff. (Currently the contact staff is Jimmy Womack, email jwomack@spp.org)

- SPP staff will verify the DNR and the mw value requested are valid based on the list submitted with the customers NITS agreement.

- Once the information is verified the request will be sent to SPP’s EMS engineering staff for creation of the sub-zone.

- Once the sub-zone is in place the reservation will be created and the reservation number will be sent to the customer.

- When the customer submits a DNR reservation for redirect the Tariff Administrator (TA) will verify the DNR is listed as an outage in SPP’s OPS1 page concurrent with the requested time frame before processing the request.

- If the request is approved and confirmed, the TA will list the DNR redirected name and time frame into a record kept on the tariff desk. This will be checked daily and OPS1 will be checked to ensure that the DNR is offline or de-rated during the redirected timeframe. If the DNR if found to be running the redirect reservation will be recalled from that point forward and any tags with the reservation on it will be terminated.

NOTE: This process will take a minimum of two weeks.