Appendix A (PSS/E)

PSS/E CHOICES IN RUNNING LOAD FLOW PROGRAM AND ACCC

BASE CASES:

Solutions – Fixed slope decoupled Newton-Raphson solution (FDNS)

- Tap adjustment – Stepping

- Area interchange control – Tie lines only

- Var limits – Apply immediately

- Solution options -    X Phase shift adjustment

_ Flat start

_ Lock DC taps

_ Lock switched shunts

ACCC CASES:

Solutions – AC contingency checking (ACCC)

- MW mismatch tolerance – 0.5

- Contingency case rating – Rate B

- Percent of rating – 100

- Output code – Summary

- Min flow change in overload report – 1mw

- Excld cases w/ no overloads form report – YES

- Exclude interfaces from report – NO

- Perform voltage limit check – YES

- Elements in available capacity table – 60000

- Cutoff threshold for available capacity table – 99999.0

- Min. contng. Case Vltg chng for report – 0.02

- Sorted output – None

Newton Solution:

- Tap adjustment – Stepping

- Area interchange control – Tie lines only

- Var limits – Apply automatically

- Solution options -    X Phase shift adjustment

_ Flat start

_ Lock DC taps

_ Lock switched shunts

Appendix A (MUST)

MUST CHOICES IN RUNNING FCITC DC ANALYSIS

CONSTRAINTS/CONTINGENCY INPUT OPTIONS

1.   AC Mismatch Tolerance – 2 MW

- Base Case Rating – Rate A

- Base Case % of Rating – 100%

- Contingency Case Rating – Rate B

- Contingency Case % of Rating – 100%

- Base Case Load Flow – PSS/E

- Convert branch ratings to estimated MW ratings – Yes

- Contingency ID Reporting – Labels

- Maximum number of contingencies to process - 50000

MUST CALCULATION OPTIONS

- Phase Shifters Model for DC Linear Analysis – Constant flow for Base Case and Contingencies

- Report Base Case Violations with FCITC – Yes

- Maximum number of violations to report in FCITC table - 50000

- Distribution Factor (OTDF and PTDF) Cutoff – 0.0

- Maximum times to report the same elements - 10

- Apply Distribution Factor to Contingency Analysis – Yes

- Apply Distribution Factor to FCITC Reports – Yes

- Minimum Contingency Case flow change – 1 MW

- Minimum Contingency Case Distribution Factor change – 0.0

- Minimum Distribution Factor for Transfer Sensitivity Analysis – 0.0