Available Flowgate Capability (AFC) Calculation Algorithms

Operating Horizon

Before 12PM noon: Current day

After 12PM noon: Current day + next day

Non-Firm AFC = TFC – Non-Firm ETC

Non-Firm AFC	Non-Firm Available Flowgate Capability

TFC			Total Flowgate Capability

Non-Firm ETC	Non-Firm Existing Transmission Commitments

Non-Firm ETC includes generation to load impacts and impacts of scheduled transmission commitments.

Planning Horizon

Day after operating horizon through day 31

Firm AFC = TFC – TRM – CBM – Firm ETC

Firm AFC		Firm Available Flowgate Capability

TFC			Total Flowgate Capability

TRM			Transmission Reliability Margin

CBM			Capacity Benefit Margin

Firm ETC		Firm Existing Transmission Commitments

Firm ETC includes generation to load impacts and impacts of firm transmission commitments.

Non-Firm AFC = TFC – Non-Firm ETC + CF

Non-Firm AFC	Non-Firm Available Flowgate Capability

TFC			Total Flowgate Capability

Non-Firm ETC	Non-Firm Existing Transmission Commitments

Non-Firm ETC includes generation to load impacts and impacts of firm and non-firm transmission commitments.

CF			Counterflow

Counterflow includes 50% of impacts of non-firm transmission commitments.

Study Horizon

Remaining of month of planning horizon through month 16

Firm AFC = TFC – TRM – CBM – Firm ETC

Firm AFC		Firm Available Flowgate Capability

TFC			Total Flowgate Capability

TRM			Transmission Reliability Margin

CBM			Capacity Benefit Margin

Firm ETC		Firm Existing Transmission Commitments

Firm ETC includes generation to load impacts and impacts of firm transmission commitments.

Non-Firm AFC = TFC – Non-Firm ETC

Non-Firm AFC	Non-Firm Available Flowgate Capability

TFC			Total Flowgate Capability

Non-Firm ETC	Non-Firm Existing Transmission Commitments

Non-Firm ETC includes generation to load impacts and impacts of firm and non-firm transmission commitments.